## Slide 1: Preliminary Research Summary
Jennifer Yang
June 14, 2021

## Slide 2: Sidewinding on Slopes
Ross L. Hatton and Howie Choset

## Slide 3: Summary
Sidewinding on slopes is unstable
Current solution: “flattening out”
  Sacrifices robustness or efficiency
Reduced model: Virtual tread model
Explore stability on slopes with respect to ellipse aspect ratios
Notes: Sidewinding on slopes is unstable
Current solution: “flattening out”
  Sacrifices robustness or efficiency
Reduced model: Virtual tread model
  Simplifies the model into rolling contact model where the backbone is a helix
  Uses the symmetry of the cylinder the model is based around to reduce the motion to that of an ellipse moving in a plane
Explore stability on slopes with respect to ellipse aspect ratios

## Slide 4: Summary
Verified with theoretical calculations and experimental data
Stability
  Backbone curve aspect ratio (ellipse aspect ratio) is a factor for determining the maximum slope
  Measured theoretically with the differences the unstable and stable branches of the equilibrium locus
  Determined maximal stable slope βmax experimentally
Notes: Verified with theoretical calculations and experimental data
Stability
  Backbone curve aspect ratio aka ellipse aspect ratio is a factor for determining the slope
  Measured theoretically with the differences the unstable and stable branches of the equilibrium locus
    Equilibrium loci occur when the COM is directly above the contact point
    Two possible measurements of stability:
      Angular stability margin
        Measured how much angular deviation can happen before rolling to a new resting angle
      Energy stability margin
        Measures how much energy disturbance can be absorbed before becoming unstable
  Determined maximal stable slope beta max experimentally
    This is the greatest slope angle that has a corresponding resting angle for that specific ellipse
      Any higher slope angles will cause the ellipse to roll down
    Determined experimentally as a function of the aspect ratio to verify the theoretical calculations

## Slide 5: Key Takeaways
Virtual tread model is a verified model for a reduced, planar version of sidewinding
  Provides a simpler, geometric calculation for the aspect ratio necessary to maintain stability
Slope angle vs aspect ratio dependency
  Angular margin depends more on slope angle
  Energy margin depends approximately equally
Notes: Virtual tread model is a verified model for a reduced, planar version of sidewinding
  Provides a simpler, geometric calculation for the aspect ratio necessary to maintain stability
  This makes it easier for us to understand movement and stability of these robots
Slope angle vs aspect ratio dependency
  Angular margin depends more on slope angle
  Energy margin depends approximately equally

## Slide 6: Questions
What does it mean to “flatten out” the sidewinding motion? What does this look like?
What is margin of stability?
Notes: ”Flatten out” – having trouble visualizing this before vs after version
Margin of stability - https://www.ncbi.nlm.nih.gov/pmc/articles/PMC3321251/
  Summary based on what I saw with that link:
    MOS is a way to account for stability in motion
    It is the distance between an extrapolated position of COM (based on velocity) (horizontally) and the edges of the BOS (base of stability) at an instance in time
    Recall stability:
      Stable if COM projection is withing horizontal BOS bounds
      Unstable otherwise

## Slide 7: An Euler-Bernoulli beam model for soft robot arms bent through self-stress and external loads
Gina Olsen, Ross L. Hatton, Julie A. Adams, Yiğit Mengüç

## Slide 8: Summary
Soft robot arm deformations make them harder to model effectively
Existing models: Cannot be generalized across designs
New model: Generalizable quasi-static bending model
  Can predict design change impacts without having to update and test the physical model
Notes: Soft robot arm deformations make them harder to model effectively
Existing models: Cannot be generalized across designs
  Reliant on parameters determined after it is built
New model: Generalizable quasi-static bending model
  Derived from Euler-Bernoulli beam theory
  Can predict design change impacts without having to update and re-test the physical model

## Slide 9: Summary
Modeled planar and spatial arms with theoretical calculations and experimental verification
  Single and two-segment planar arms
  Single-segment spatial arms
Key assumptions
  Loads are limited to bend plane
  Deformation is quasi-static
Notes: Modeled planar and spatial arms with theoretical calculations and experimental verification
  Single and two-segment planar arms
    These were tested with assorted widths
  Single-segment spatial arms
    This was tested with one width
    A multi-segment spatial arm was not tested
Key assumptions
  Many assumptions were made but the most important ones are the following
    Loads are limited to bend plane
    Deformation is quasi-static

## Slide 10: Key Takeaways
This model is generalizable, allowing for design changes and evaluation prior to manufacturing
Soft arms under loads demonstrate the following:
  Nonconstant curvature
  Compression under loads
Kinematic modeling
  Piecewise Constant Curvature (PCC) is most common
  Inverse models must have compatibility constraints
Notes: This model is generalizable, allowing for design changes and evaluation prior to manufacturing
  Can predict design change results, internal stresses, and external loads
Soft arms under loads demonstrate the following:
  Nonconstant curvature
  Compression under loads
    This includes when the loads weren’t inherently compressive too
Kinematic modeling
  Piecewise Constant Curvature (PCC) is most common
    A limitation of this is that it can only capture the deformed shape if each segment has been modeled as multiple kinematic links with known curvatures and stretches
  Inverse models must have compatibility constraints
    Lack of a compatibility constraint means that there is no guarantee that it will reach the required state
    Currently a challenge to figure out quickly

## Slide 11: Questions
Are there any videos that show how the physical model worked and how it was tested?
Notes: Honestly just would like to visualize this more bc I think that would help

## Slide 12: Possible Avenues of Research

## Slide 13: Possible Avenues of Research
How can different McKibben actuator-based arm setups be modeled and utilized in sidewinding?
  Exploring different combinations of planar segments or spatial segments and their movement
  Exploring movement across more varied terrain
  Generalizing the McKibben actuator-based model to not be loaded strictly in the bend plane
Notes: How can different McKibben actuator-based arm setups be modeled and utilized in sidewinding?
  In general, how can we get the McKibben actuator format to work for sidewinding and has that been tested?
  Some specifics for things that we could experiment with are the following:
    Exploring different combinations of planar segments or spatial segments and their movement
      So different segment widths and lengths, segment setups, etc
    Exploring movement across more varied terrain
      Instead of sidewinding on slopes, what about a sidewinding motion to traverse steps? In general just looking at more rough terrain
    Generalizing the McKibben actuator-based model to not be loaded strictly in the bend plane
      The McKibben paper mentioned that this was restricted to the bend plane which is a limitation
      What if that limitation was removed to extend it to a general rod theory like the paper says?
      How would that look and how would that impact sidewinding motion?